1) find transfer function H(s)

I_1 = I_2 + I_3

left ( {Vin – Vout} over R right)= left( C dVout over dt right) +left( 1 over L int [ Vout dt] right)

R C dVout over dt +Vout + R over L int [Vout dt] = Vin

laplace left lbrace R C dVout over dt +Vout + R over L int [Vout dt] right rbrace = laplace lbrace Vin rbrace

R C left(s tilde Vout + Vout(0) right) + left( tilde Vout right)+ R over L left( 1 over s tilde Vout right) = tilde Vin

lets Vout(0) = 0 as the transfer function is defined under a zero state condition.

R C s tilde Vout + tilde Vout+ R over {L s }tilde Vout = tilde Vin

left ( R C s+1+ R over {L s } right ) tilde Vout = tilde Vin

left ( R C s+1+ R over {L s } right ) tilde Vout over tilde Vin = 1

tilde Vout over tilde Vin = 1 over left ( R C s+1+ R over {L s } right )

tilde Vout over tilde Vin = {L s } over left ( R C L s^2 +Ls+ R right )

H(s) = {L s } over left ( R C L s^2 +Ls+ R right )

2) find impulse response h(t)

Vin = δ(t) → tilde Vin = 1 → H(s) = tilde Vout

laplace lbrace h(t) rbrace = {L over {R C L } s } over left (s^2 +L over {R C L }s+ R over {R C L } right )

laplace lbrace h(t) rbrace = {1 over {R C } s } over left (s^2 +1 over {R C }s+ 1 over { C L } right )

laplace lbrace h(t) rbrace = {1 over {R C } s } over left (left (s +1 over {2 R C } right)^2 - left (1 over {2 R C } right)^2+ 1 over {C L } right )

let ω^2 = 1 over {C L }- left (1 over {2 R C } right)^2
let α = 1 over {2 R C}

laplace lbrace h(t) rbrace = {2α s } over {left (s +α right)^2 + ω^2 }

laplace lbrace h(t) rbrace = 2α left ({ s } over {left (s +α right)^2 + ω } right)

laplace lbrace h(t) rbrace = 2α left ({s + α – α} over {left (s +α right)^2 + ω^2 } right)

laplace lbrace h(t) rbrace = 2α left ({s + α } over {left (s +α right)^2 + ω^2 } + { – α} over {left (s +α right)^2 + ω^2 } right)

laplace lbrace h(t) rbrace = 2α left ({s + α } over {left (s +α right)^2 + ω^2 }right) + 2α left ({ – α} over {left (s +α right)^2 + ω^2 } right)
laplace lbrace h(t) rbrace = 2α left ({s + α } over {left (s +α right)^2 + ω^2 }right) - 2α^2 left ({ 1} over {left (s +α right)^2 + ω^2 } right)

laplace lbrace h(t) rbrace = 2α left ({s + α } over {left (s +α right)^2 + ω^2 }right) - 2α^2 left ({ ω over ω} over {left (s +α right)^2 + ω^2 } right)

laplace lbrace h(t) rbrace = 2α left ({s + α } over {left (s +α right)^2 + ω^2 }right) - 2α^2 over ω left ({ ω } over {left (s +α right)^2 + ω^2 } right)

h(t) = 2α e^{-αt} cos(ω t) u(t)- 2α^2 over ω e^{-αt} sin(ω t) u(t)

let ω^2 = 1 over { C L }- left (1 over {2 R C } right)^2
let α = 1 over {2 R C}

h(t) = 2 1 over {2 R C} e^{-1 over {2 R C} t} cos left ( sqrt {1 over {C L }- left (1 over {2 R C } right)^2 }t right) u(t)- 2 left( 1 over {2 R C} right)^2 over sqrt {1 over { C L }- left (1 over {2 R C } right)^2 } e^{- 1 over {2 R C} t} sin left (sqrt {1 over {C L }- left (1 over {2 R C } right)^2 } t right) u(t)

h(t) = 1 over { R C} e^{-1 over {2 R C} t} cos left ( sqrt {1 over {C L }- left (1 over {2 R C } right)^2 }t right) u(t)- {2 left( 1 over {2 R C} right)^2} over sqrt {1 over { C L }- left (1 over {2 R C } right)^2 } e^{- 1 over {2 R C} t} sin left (sqrt {1 over {C L }- left (1 over {2 R C } right)^2 } t right) u(t)

for the given values: R = 1000 Ω, L = 0.027 H, and C = 10E-9 F

h(t) = 100000 e^{-100000 t} cos left ({50000 sqrt 39} over 9 t right) u(t)- {300000 sqrt 39} over {13} e^{- 100000 t} sin left ({50000 sqrt 39} over 9 t right) u(t)

or approximately

h(t) = 100000 e^{-100000 t} cos left (34694.4 t right) u(t)- 144115 e^{- 100000 t} sin left (34694.4 t right) u(t)

or

h(t) = 175412 e^{-100000 t} cos left (34694.4 t+55.2437 ° right) u(t)