x_0(t) = 2 P_{T/2} (t-T/4)- 1

x(t) = 1 over 2 a_0 + sum from k=1 to ∞ left[ a_k cos left(k {2π} over T t right) + b_k sin left(k {2π} over T t right) right]

a_k = 2 over T int from 0 to T left [ x(t) cos left (k {2 π} over T t right )dt right ]

b_k = 2 over T int from 0 to T left [ x(t) sin left (k {2π} over T t right )dt right ]

a_0 = 2 over T int from 0 to T left [ x(t) dt right ]

finding a_0
a_0 = 2 over T int from 0 to T left [ x(t) dt right ]

a_0 = 2 over T (0)

a_0 = 0

finding a_k
a_k = 2 over T int from 0 to T left [ (2 P_{T/2} (t-T/4)- 1) cos left (k {2π} over T t right )dt right ]

a_k = 2 over T int from 0 to T left [ 2 P_{T/2} (t-T/4) cos left (k {2π} over T t right )dt right ] - 2 over T int from 0 to T left [ cos left (k {2π} over T t right )dt right ]

a_k = 2 over T int from 0 to T left [ 2 u(t) cos left (k {2π} over T t right )dt right ] -2 over T int from 0 to T left [ 2 u left(t-t over 2 right) cos left (k {2π} over T t right )dt right ] - 2 over T int from 0 to T left [ cos left (k {2π} over T t right )dt right ]

a_k = 2 over T int from 0 to T left [ 2 cos left (k {2π} over T t right )dt right ] -2 over T int from 0 to T left [ 2 u left(t-t over 2 right) cos left (k {2π} over T t right )dt right ] - 2 over T int from 0 to T left [ cos left (k {2π} over T t right )dt right ]
a_k = 2 over T int from 0 to T left [ 2 cos left (k {2π} over T t right )dt right ] -2 over T int from T/2 to T left [ 2 cos left (k {2π} over T t right )dt right ] - 2 over T int from 0 to T left [ cos left (k {2π} over T t right )dt right ]

a_k = 2 over T int from 0 to T/2 left [ 2 cos left (k {2π} over T t right )dt right ] - 2 over T int from 0 to T left [ cos left (k {2π} over T t right )dt right ]

a_k = 2 over T int from 0 to T/2 left [ 2 cos left (k {2π} over T t right )dt right ]- 2 over T evaluate left [ 1 over {k {2π} over T} sin left( k {2π} over T t right) right] from 0 to T

a_k = 2 over T int from 0 to T/2 left [ 2 cos left (k {2π} over T t right )dt right ] - 2 over T 1 over {k {2π} over T} evaluate left [ sin left( k {2π} over T t right) right] from 0 to T

a_k = 2 over T int from 0 to T/2 left [ 2 cos left (k {2π} over T t right )dt right ] - 2 over T T over {k {2π}} evaluate left [ sin left( k {2π} over T t right) right] from 0 to T

a_k = 2 over T int from 0 to T/2 left [ 2 cos left (k {2π} over T t right )dt right ] - 1 over {k π} evaluate left [ sin left( k {2π} over T t right) right] from 0 to T

a_k = 2 over T int from 0 to T/2 left [ 2 cos left (k {2π} over T t right )dt right ] - 1 over {k π} left [ sin left( k {2π} over T (T) right) - sin left( k {2π} over T (0) right) right ]

a_k = 2 over T int from 0 to T/2 left [ 2 cos left (k {2π} over T t right )dt right ] - 1 over {k π} left [ sin left( k {2π} over T (T) -0 right) right ]

a_k = 2 over T int from 0 to T/2 left [ 2 cos left (k {2π} over T t right )dt right ] - 1 over {k π} left [sin left( k {2π} right)- 0 right ]

a_k = 2 over T int from 0 to T/2 left [ 2 cos left (k {2π} over T t right )dt right ] - 1 over {k π} left [ 0- 0 right ]

a_k = 2 over T int from 0 to T/2 left [ 2 cos left (k{ 2π} over T t right )dt right ]

a_k = 4 over T int from 0 to T/2 left [ cos left (k {2π} over T t right )dt right ]

a_k = 4 over T evaluate left [1 over {k {2π} over T} sin left (k {2π} over T t right )right ] from 0 to {T/2}

a_k = 4 over T 1 over {k {2π} over T} evaluate left [ sin left (k {2π} over T t right )right ] from 0 to {T/2}

a_k = 2 over {k π} evaluate left [ sin left (k {2π} over T t right )right ] from 0 to {T/2}

a_k = 2 over {k π} left [ sin left (k {2π} over T (T/2) right ) - sin left (k {2π} over T (0) right )right ]

a_k = 2 over {k π} left [ sin left (k {2π} over T (T/2) right ) - 0 right ]

a_k = 2 over {k π} left [ sin left (k π right ) - 0 right ]

a_k = 2 over {k π} left [ 0 - 0 right ]

a_k = 0

finding b_k
b_k = 2 over T int from 0 to T left [ (2 P_{T/2} (t-T/4)- 1) sin left (k {2π} over T t right )dt right ]

b_k = 2 over T int from 0 to T left [ 2 P_{T/2} (t-T/4) sin left (k {2π} over T t right )dt right ] - 2 over T int from 0 to T left [ sin left (k {2π} over T t right )dt right ]

b_k = 2 over T int from 0 to T left [ 2 u(t) sin left (k {2π} over T t right )dt right ] - 2 over T int from 0 to T left [ 2 u left (t-T over 2 right ) sin left (k {2π} over T t right )dt right ] - 2 over T int from 0 to T left [ sin left (k {2π} over T t right )dt right ]

b_k = 2 over T int from 0 to T left [ 2 u(t) sin left (k {2π} over T t right )dt right ] - 2 over T int from {T/2} to T left [ 2 sin left (k {2π} over T t right )dt right ] - 2 over T int from 0 to T left [ sin left (k {2π} over T t right )dt right ]

b_k = 2 over T int from 0 to T left [ 2 sin left (k {2π} over T t right )dt right ] - 2 over T int from {T/2} to T left [ 2 sin left (k {2π} over T t right )dt right ] - 2 over T int from 0 to T left [ sin left (k {2π} over T t right )dt right ]

b_k = 2 over T int from 0 to {T/2} left [ 2 sin left (k {2π} over T t right )dt right ] - 2 over T int from 0 to T left [ sin left(k {2π} over T t right )dt right ]

b_k = 2 over T evaluate left [ -2 over {k {2π} over T } cos left (k {2π} over T t right ) right ]from 0 to {T/2} - 2 over T int from 0 to T left [ sin left(k {2π} over T t right )dt right ]

b_k = -2 over {k π } evaluate left [ cos left (k {2π} over T t right ) right ]from 0 to {T/2} - 2 over T int from 0 to T left [ sin left(k {2π} over T t right )dt right ]

b_k = -2 over {k π } left [ cos left (k {2π} over T (T/2) right ) -cos left (k {2π} over T (0) right ) right ] - 2 over T int from 0 to T left [ sin left(k {2π} over T t right )dt right ]

b_k = -2 over {k π } left [ cos left (k {2π} over T (T/2) right ) -1 right ] - 2 over T int from 0 to T left [ sin left(k {2π} over T t right )dt right ]

b_k = -2 over {k π } left [ cos left (k π right ) -1 right ] - 2 over T int from 0 to T left [ sin left(k {2π} over T t right )dt right ]

b_k = -2 over {k π } left [ (-1)^k -1 right ] - 2 over T int from 0 to T left [ sin left(k {2π} over T t right )dt right ]

b_k = -2 over {k π } left [ (-1)^k -1 right ] - 2 over T evaluate left [ -1 over {k {2π} over T } cos left (k {2π} over T t right ) right ]from 0 to {T}

b_k = -2 over {k π } left [ (-1)^k -1 right ] - -1 over {k {π} } evaluate left [cos left (k {2π} over T t right ) right ]from 0 to {T}

b_k = -2 over {k π } left [ (-1)^k -1 right ] - -1 over {k {π} } left [cos left (k {2π} over T (T) right ) - cos left (k {2π} over T (0) right ) right ]

b_k = -2 over {k π } left [ (-1)^k -1 right ] - -1 over {k {π} } left [cos left (k {2π} over T (T) right ) - 1 right ]

b_k = -2 over {k π } left [ (-1)^k -1 right ] - -1 over {k {π} } left [cos left (k 2π right ) - 1 right ]

b_k = -2 over {k π } left [ (-1)^k -1 right ] - -1 over {k {π} } left [1 - 1 right ]

b_k = -2 over {k π } left [ (-1)^k -1 right ] - -1 over {k {π} } left [0 right ]

b_k = -2 over {k π } left [ (-1)^k -1 right ]

finding

x(t) = 1 over 2 (0) + sum from k=1 to ∞ left[ (0) cos left(k {2π} over T t right) + left(-2 over {k π } left [ (-1)^k -1 right ] right) sin left(k {2π} over T t right) right]

x(t) = sum from k=1 to ∞ left[ left(-2 over {k π } left [ (-1)^k -1 right ] right) sin left(k {2π} over T t right) right]

x(t) = -2 over { π } sum from k=1 to ∞ left[ left(1 over {k} left [ (-1)^k -1 right ] right) sin left(k {2π} over T t right) right]

x(t) = -2 over { π } sum from k=1 to ∞ left[ left(1 over {k} left [ (-1)^k -1 right ] right) sin left(k {2π} over T t right) right]

x(t) = 2 over { π } sum from k=1 to ∞ left[ left(1 over {k} left [1- (-1)^k right ] right) sin left(k {2π} over T t right) right]

let k = 2n-1

x(t) = 2 over { π } sum from { 2n-1=1} to ∞ left[ left(1 over { 2n-1} left [1- (-1)^( 2n-1) right ] right) sin left(( 2n-1) {2π} over T t right) right]

x(t) = 2 over { π } sum from { 2n=2} to ∞ left[ left(1 over { 2n-1} left [1- (-1)^( 2n-1) right ] right) sin left(( 2n-1) {2π} over T t right) right]

x(t) = 2 over { π } sum from { n=1} to ∞ left[ left(1 over { 2n-1} left [1- (-1)^( 2n-1) right ] right) sin left(( 2n-1) {2π} over T t right) right]

x(t) = 2 over { π } sum from { n=1} to ∞ left[ left(1 over { 2n-1} left [1- (-1)^( 2n)(-1) right ] right) sin left(( 2n-1) {2π} over T t right) right]

x(t) = 2 over { π } sum from { n=1} to ∞ left[ left(1 over { 2n-1} left [1+ (-1)^( 2n) right ] right) sin left(( 2n-1) {2π} over T t right) right]

x(t) = 2 over { π } sum from { n=1} to ∞ left[ left(1 over { 2n-1} left [1+ ((-1)^2)^n right ] right) sin left(( 2n-1) {2π} over T t right) right]

x(t) = 2 over { π } sum from { n=1} to ∞ left[ left(1 over { 2n-1} left [1+1^n right ] right) sin left(( 2n-1) {2π} over T t right) right]

x(t) = 2 over { π } sum from { n=1} to ∞ left[ left(1 over { 2n-1} left [1+1 right ] right) sin left(( 2n-1) {2π} over T t right) right]

x(t) = 2 over { π } sum from { n=1} to ∞ left[ left(1 over { 2n-1} left [1 right ] right) sin left(( 2n-1) {2π} over T t right) right]

x(t) = 2 over { π } sum from { n=1} to ∞ left[ left(2 over { 2n-1} right) sin left(( 2n-1) {2π} over T t right) right]

x(t) = 4 over { π } sum from n=1 to ∞ left[ left(1 over {2n-1} right) sin left((2n-1) {2π} over T t right) right]